# EarthCraft Multifamily Home Energy Rating System (HERS) Summary:

Project, Date

The following construction specifications were used when completing the energy model (HERS rating v12.95).  A HERS rating was conducted using a worst case unit level model based on an analysis of window to floor area ratios and exterior wall areas.  The results of passing and failing units are identified on the following page along with a summary of the improvement analysis. If any of the following elements are altered please notify the EarthCraft Technical Advisor so the models may be updated to reflect changes.

Building Shell

| Assembly | Insulation Value |
| --- | --- |
| Flat Ceilings | R-38 |
| Above grade exterior walls | R-13 |
| Exterior band area | R-13 |
| Floors over unconditioned space | NA |
| Window U value and SHGC | U-.40, SHGC- .40 |
| Tenant Entrance Door | R-7 |

Mechanical Systems/Lighting

| Appliance | Efficiency |
| --- | --- |
| Water Heater: | 40 gal, .95 Ef |
| Heat Pump: | 8.5 HSPF, 14 SEER |
| Ducts in unconditioned space | R-8 |
| Programmable Thermostat | Yes |
| Fluorescent Lighting | Pin Based 10%, Compact fluorescent 20% |
| Refrigerator | 388 kWh/yr |
| Dishwasher | 70. EF |
| Ceiling Fan | Default- 75 CFM/watt |

Infiltration and Duct Leakage

| Test | Results |
| --- | --- |
| Blower Door (infiltration test) | <0.35 CFM50 per sq ft of building envelope |
| Duct Blaster (duct leakage test) | <6% CFM25 per sq ft of floor area |

Improvement Analysis Results:

Unit:

HERS Index:

| Improvement Strategy | Index |
| --- | --- |

Unit:

HERS Index:

| Improvement Strategy | Index |
| --- | --- |

Units Passing HERS Index requirement:

| Unit Type | Index |
| --- | --- |

Based on current building component specifications outlined on page 1.